## Slide 1: BTP (2-Bromo-3,3,3-Trifluoropropene) Status Update
PRESENTATION TO:
Federal Aviation Administration
IASFPWG
and
International Civil Aviation Organization
November 14-16, 2012
Bradford Colton
American Pacific Corp.
bcolton@apfc.com

## Slide 2: Quick Refresher - Chronology
BTP (“NMERI 873”) was developed under the funding of the Advanced Agent Working Group, whose membership included (select members):
  New Mexico Research Institute (NMERI)
  NIST, under their Next Generation Program
  US Environmental Protection Agency
  British Petroleum
  DuPont
  Kidde Research UK
  NASA
  American Pacific
Original intent was to find a Halon 1301 replacement total flooding agent, but BTP was the best compound to meet identified requirements
  Contained bromine to improve effectiveness
  Short atmospheric lifetime so that Ozone Depletion Potential values would be negligible in terms of stratospheric impact

## Slide 3: Chronology – First Production, Cargo and Engine Tests
In 2001, AMPAC made the first batches that were larger than lab scale
  It quickly became apparent that the material reacted with any air and moisture in storage tanks and became acidic
  A two year project identified stabilizers needed in order to make the material commercially viable
Based on positive small scale bulk load tests performed by Kidde Research, BTP was sponsored for FAA Cargo testing in 2003
  Determined that under lean concentrations, BTP, Novec 1230, and HFC-125 can be made combustible in the Exploding Aerosol Can Test
  Other cargo tests not completed
  The unique setup of this test is a non-issue for use of BTP in handhelds
Some engine testing was conducted in 2004
  Fire well extinguished, but appeared to sometimes increase re-ignition intensity
  Testing stopped by sponsor before completion

## Slide 4: Handheld Tests – Outstanding Performance
Agent development on hold until 2009
  Aviation industry need for weight and space reductions beyond that offered by existing approved agents
  BTP fire fighting performance greater than any other commercialized Halon 1211 replacement (other than FM-100, abandoned by 1994)
Formal UL fire testing in late 2009 (according to UL 711 and FAA MPS)
  Extinguisher size fits envelope of current 2.5 Lb. Halon 1211 model Boeing uses
  3.75 Lb. net charge weight BTP extinguisher passed these fire performance tests
    Hidden fire test
    5B pan fire extinguished three times consecutively, as required by UL 711
    2B pan fire with extinguisher conditioned at -40°C
  FAA seat/fire toxicity testing in 2011
    Acceptable acid gas levels

## Slide 5: BTP – 5B Fire Video

## Slide 6: BTP – Hidden Fire Test Video

## Slide 7: BTP – Seat Fire Test

## Slide 8: Properties With Comparisons
 | HALON 1211 | BTP (2) | HALOTRON I
Chemical Formula | CF2ClBr | CF3CBr=CH2 | CF3CHCl2 + gases (Ar, CF4)
Molecular Weight | 165.4 | 174.9 | 150.7
Ozone Depletion Potential (CFC-11 = 1) | 7.9 | <0.0028 for U.S. and E.U. | 0.0098
Global Warming Potential (100 yr. time horizon, CO2 = 1) | 1,890 | 0.26 for U.S. and E.U. ***UPDATED**** | 77 (1)
Atmospheric Lifetime | 16 years | 7 days | 1.3 years (1)
Boiling Point @ 1 Atm. | 26 ºF (-3 ºC) | 93 ºF (34 ºC) | 81 ºF (27 ºC)
LC 50 (4 hr rat) | 31,000 – 100,000 ppm | > 20,000 ppm | 30,000 – 35,000 ppm
Cardio-Tox LOAEL | 1%vol. | 1%vol. | 2%vol.
Cardio-Tox NOAEL | 0.5%vol. | 0.5%vol. | 1%vol.
Fire Class Effectiveness | ABC | ABC | ABC
Cup Burner, heptane | 3.2%vol. | 4.7%vol. | 6.5%vol.
Allowed for Training | No | Yes when SNAP listed | Yes
Based on HCFC-123. Also contains one PFC in small proportion There is no global average ODP or GWP due to short lifetime – values depend on latitude. |  |  | 

## Slide 9: Ongoing Work – Toxicity Profile
Fire performance and acute fire fighter exposure data has been established
  Material cannot be approved without additional toxicology and physical property testing
  Boeing sponsoring most of the additional testing required for regulatory approval
Test program includes such tests as:
  Rat Micronucleus
  Eye Irritation
  Skin irritation
  Acute Dermal
  90-day Sub-Chronic Inhalation
  Reproductive and Development Screen
  Acute Fish Toxicity
  Activated Sludge Respiration Inhibition
  Biodegradation

## Slide 10: Schedule – Path to Possible Commercialization
Toxicology tests are starting to wrap up with major results due 1Q2013
Pending acceptable testing results, US EPA SNAP and EU ECHA REACH submittal in 2Q2013
Regulatory review expected to be complete by end of 2013
  US Federal Register notice may take longer
2012 – 2013: Complete additional UL functional tests such as 1 year leak test, minimum and maximum temperature intermittent discharges, 30-day elevated temperature, etc…
Commercialization for aviation shortly after US and EU approvals