## Slide 1: Formulation of Petroleum and Alternative – Jet Fuel Surrogates
Peter S. Veloo
Exponent, Failure Analysis Associates, Los Angeles, CA
Sang Hee Won & Frederik L. Dryer
Department of Mechanical and Aerospace Engineering, Princeton University, NJ
Stephen Dooley
Department of Chemical and Environmental Sciences, University of Limerick, Ireland
The 7th International Aircraft Fire and Cabin Safety Research Conference
Philadelphia, PA
5th December 2013

## Slide 2: Gas Turbines and Chemical Kinetics
Coupling chemical kinetics and computational fluid mechanics for engine design
Kinetically limited processes
  Nitrogen oxide production
  Soot formation
  Flame stability
  Blow out
J Campbell, J. Chambers, Patterns in the sky: natural visualization of aircraft ﬂow ﬁelds. NASA SP-514,1994
Notes: Why we care about chemical kinetics

## Slide 3: Aviation Fuels – Composition
Distillation Temperature
Carbon Number Distributions
Hydrocarbon Class Distribution
T. Edwards, L.Q. Maurice, J. Propulsion Power 17 (2001)
JP-4
JP-8
JP-7
Cycloparafins
n-Parafins
Naphthalenes
i-Parafins
Alkylbenzenes
Notes: What is the problem I
Methylnaphtalene

## Slide 4: Aviation Fuels – Fuel Variability
Chart: Volume %
| 12 | 14 | 16 | 18 | 20 | 22 | 24
 | 2.96 | 7.8 | 19.39 | 19.53 | 36.94 | 10.79 | 2.19
Aromatics Content
Chart: Cetane Index
| 36 | 39 | 42 | 45 | 48 | 51
 | 2.66 | 3.68 | 13.25 | 45.55 | 28.87 | 5.5
Cetane Index
Significant variability in physical and chemical properties
Current certification not highly constraining
Petroleum Quality Information System Annual Report (2009)
Fraction of delivered JP-8 fuels with specified properties
Notes: What is the problem II

## Slide 5: Surrogate Fuel Concept
Computational fluid dynamics coupled with detailed chemical kinetics requires a simplified fuel model
Real Fuel
Surrogate Fuel
Abundance
Distillation Temperature
Ideal surrogate fuel must emulate combustion behavior and physical properties of a target real fuel
Notes: Introduce Concept of surrogate fuels

## Slide 6: Surrogate Fuels – Previous Work
Numerous jet fuel surrogate postulations present in literature (e.g.):
  Sarofim et al. ─ Surrogate fuel to model jet fuel pool fires
  Bruno et al. ─ Surrogate fuel to model thermo-physical properties of jet fuel
Require detailed characterizations of target fuel (GC, NMR, …)
Significant uncertainty in chemical kinetics of selected surrogate compounds
Sarofim et al., Combust. Sci. Tech, 177 (2005) 715–739
T.J. Bruno et al., Ind. Eng. Chem. Res 45 (2006) 4371–4380
Notes: Brief overview of state of surrogate modeling field/ limitations of the method

## Slide 7: Surrogate Fuels – Present Approach
GOAL: Emulate gas phase combustion behavior of a target jet fuel
Notes: Our Strategy – critical fuel property targets

## Slide 8
C4
C3
C2
C1
CH3O C2H5 C2H3 CH3O2
CH3 HCO HO2
H O OH
Real fuels – Many generic initial chemical functionalities
Fewer distinct chemical functionalities after initial oxidation
Distinct functionalities govern radical and small species concentrations
Surrogate fuel need only reproduce:
distinct chemical functionalities
Notes: Theory of Our Particular Methodology and Why it works

## Slide 9: Surrogate Fuels – Present Approach
GOAL: Emulate gas phase combustion behavior of a target jet fuel
Identified critical combustion property targets:
  Adiabatic flame temperature
  Enthalpy of combustion
  Flame speed / burning rate
  Fuel diffusive properties
  Sooting propensity
  Auto-ignition
Manifest in important practical combustion behavior
Surrogate fuel must emulate critical fuel properties of target real fuel

## Slide 10: Surrogate Fuels – Present Approach
Quantify critical fuel property targets:
  Adiabatic flame temperature
  Enthalpy of combustion
  Flame speed / burning rate
  Fuel diffusive properties
  Sooting propensity
  Auto-ignition
The ratio of hydrogen to carbon (H/C)
-CHN analysis (ASTM D5291)
Smoke point measurement (ASTM D1322)
Average molecular weight (MWavg)
Derived cetane number (ASTM D6890)
Notes: Our Strategy – critical fuel property targets

## Slide 11: Case Study 1 – Fuel Surrogate for Jet A
n-Alkanes
28%
cyclo-Alkanes
20%
iso-Alkanes
29%
Alkylbenzenes
18%
Naphthlenes
2%
Selected Surrogate Fuel
Components
n-Dodecane
iso-Octane
n-Propylbenzene
1,3,5-Trimethylbenzene
Dooley et al., Combust Flame (2010) 157:2333-2339
Dooley et al., Combust Flame (2012) 159: 1444-4466
Notes: CASE STUDY I – Formulating a surrogate for a typical Jet A – overview of composition and selection of surrogate compounds

## Slide 12: Surrogate Fuel Formulation Algorithm
Characterize target Jet A
Characterize surrogate components and their mixtures
Emulate H/C, DCN, TSI, MWavg
Compare gas phase combustion characteristics between surrogate and target
Experimental observations
Intermediate species profiles
Flame speeds / extinction limits
Soot volume fraction
Ignition delay times
Regression analysis to determine surrogate composition
Characterize target Jet A
H/C
Cetane number
Smoke point
Average molecular weight
Develop library of target measurements for individual and mixtures of surrogate components
Notes: Algorithm for generating surrogate mixture

## Slide 13: Surrogate Fuel Compared with Real Jet-A Fuel
Equivalence Ratio, f
Chart: 
| 0.69963000000000031 | 0.80075000000000029 | 0.89900000000000002 | 0.99717 | 1.0995599999999999 | 1.2047399999999993 | 1.2984599999999999 | 1.4006899999999998
 | 40.9997 | 50.4538 | 59.1407 | 62.4535 | 63.8465 | 62.1681 | 54.8614 | 47.2977
 | 42.279 | 51.9895 | 60.6759 | 63.7327 | 64.6138 | 61.0171 | 54.7331 | 45.251
 - Jet A
 - Surrogate
Laminar Flame Speed, cm/s
p = 1 atm, Tu =400 K
Laminar Flame Speeds
Dooley et al., Combust Flame (2010) 157:2333-2339
Dooley et al., Combust Flame (2012) 159: 1444-4466
Notes: Brief overview of experimental validation – all avenues

## Slide 14: Surrogate Fuel Compared with Real Jet-A Fuel
Extinction Strain Rate, s-1
Fuel Mass Fraction, XY
 - Jet A
 - Surrogate
Extinction Limits
Dooley et al., Combust Flame (2010) 157:2333-2339
Dooley et al., Combust Flame (2012) 159: 1444-4466
Notes: What the counterflow configuration allows us to validate (laminar flame velocities, flame extinction (premixed, diffusion flames), flame ignition (premixed, diffusion, partial premixed))

## Slide 15: Surrogate Fuel Compared with Real Jet-A Fuel
Soot Volume Fraction
 - Jet A
 - Surrogate
Radial Location (mm)
Soot Volume Fraction (ppm)
Dooley et al., Combust Flame (2010) 157:2333-2339
Dooley et al., Combust Flame (2012) 159: 1444-4466
Notes: Back to case study 1 – results of Surrogate fuel vs Real fuel – flame speeds and detailed speciation

## Slide 16: Case Study 2 – Fuel Surrogate for S-8
Mono-methylated
Alkanes
61%
Di-methylated
Alkanes
25%
Normal-Alkanes
12%
Selected Surrogate Fuel
Components
n-Dodecane
iso-Octane
Dooley et al., Combust Flame (2012) 159: 3014-3020
Notes: CASE STUDY II – alternative aviation fuel

## Slide 17: Surrogate Fuel Compared with Real S-8
1000K/T
Ignition Delay Time
Shock tube ignition delay times
Dooley et al., Combust Flame (2012) 159: 3014-3020
Notes: Identify the problem – pyrolysis products from polymers – how to model? – select set of compounds that represent the same functional groups present during the pyrolysis of the polymer
Show some pictures identifying products what do we understand well?????

## Slide 18: Chemical Kinetic Modeling
Large spread in predictions using latest chemical kinetic reaction models for surrogate components
  Lack of consensus within kinetic modeling community

## Slide 19: Uncertainties in Numerical Calculations
Propagation of uncertainties from rate parameters to numerical simulations
Numerical
Uncertainty

## Slide 20: Concluding Remarks
Demonstrated surrogate fuel methodology to capture gas phase combustion behavior of aviation fuels
Reaction model rate parameter uncertainties require further reduction
Application of surrogate concept to polymer combustion
  Determine surrogates that represent functionalities present in gas phase pyrolysis products
Notes: Concluding Remarks