## Slide 1: Performance of a Numerical Model of the ES-2re as a Function of Impact Angle
IAFCSRC
David Moorcroft
5 December 2013

## Slide 2: Side-Facing Seats
FAA Policy (PS-ANM-25-03-R1) requires testing with the ES-2re for purely side-facing seats
Evaluates risk of injury to head, neck, ribs (from contact and shoulder strap loads), abdomen, pelvis, and legs
Photo courtesy of Cessna

## Slide 3: ES-2re
The ES-2re was specifically designed for lateral loading
  Rib deflection instrumentation is designed for unilateral motion
  Solid rubber abdomen casing

## Slide 4: ES-2re Injury Criteria
Head: HIC < 1000 (23% risk of AIS 3+ head injury)
Upper Neck Tension Force < 405 lb (25% risk of AIS 3+ neck injury)
Upper Neck Compressive Force < 405 lb
Upper Neck Torque (x-axis) < 1018 in-lb
Upper Neck Shear < 186 lb
Upper Torso Strap Load < 1750 lb (50% risk of AIS 3+ chest injury)

## Slide 5: ES-2re Injury Criteria
Upper, Middle, Lower Rib deflection < 1.73” (50% risk of AIS 3+ chest injury)
Front+Middle+Rear Abdominal Force < 562 lb (33% risk of AIS 3+ abdominal injury)
Pubic Symphysis Force < 1,350 lb (25% risk of AIS 3+ pelvic injury)
Lower Leg Flail Limit (35°)
Restraints must remain on ATD
Occupant Support Criteria

## Slide 6: Obliquely-Mounted Seats
Obliquely-oriented seats presents a novel loading environment that may permit significant flailing with off-axis loading
An ATD capable of evaluating injury risks due to combined forward and lateral loading is necessary
Delta

## Slide 7: Obliquely-Mounted Seats
Current forward-facing ATDs cannot measure all the likely injuries
Construction of the ES-2re may not hold up to significant forward flail
Jet Airways

## Slide 8: Oblique Flail: FAA-Hybrid III + Armrest

## Slide 9: Methods
v-ATD of ES-2re (left-hand configuration)
Wall configuration and restraint system similar to 2005 CAMI tests
  Report number: AM-07/13
Instrumentation per side-facing policy
Pulse applied from 90° to 30°(15° increments)
14 CFR Part 25.562 Test 2 pulse (16g peak, 90 ms rise time, 44 ft/s velocity change)
Simulations with and without shoulder strap
  No strap is worst case for ineffective shoulder strap

## Slide 10: Full Body Support Body-Centered Restraint

## Slide 11: Full Body Support Body-Centered Restraint

## Slide 12: Wall Placement
Numerical ES-2re arms stick out further than physical ATD
Moved wall 1” outboard to accommodate
Delays head contact
CAMI Wall
Virtual Wall
10”

## Slide 13: Point Comparison
Madymo 7.4.1
ES-2re
  Quality-rate facet model, version 3.0.2
  Left hand model
Test case: 90°
  Full body support (wall), body-centered restraint
All other scenarios are an extrapolation
Point comparison provides limited confidence in model at other angles

## Slide 14: Shoulder Strap, 90° Simulation

## Slide 15: Test-Simulation Comparison
Injury Criteria | Limit | Test (A05065) | Simulation
HIC | 1000 | 537 | 770
Upper Neck Tension (lb) | 405 | 140 | 213
Upper Neck Compression (lb) | 405 | 162 | 152
Upper Neck Shear (lb) | 186 | 103 | 117
Upper Neck Torque (in-lb) | 1018 | 141 | 99
Upper Rib Deflection (in) | 1.73 | 1.1 | 0.70
Middle Rib Deflection (in) | 1.73 | 0.75 | 0.50
Lower Rib Deflection (in) | 1.73 | 0.55 | 0.32
Abdominal Forces (lb) | 562 | 45 | 134
Pubic Symphysis Force (lb) | 1350 | 203 | 748
Shoulder Strap Load (lb) | 1750 | 41 | 333

## Slide 16: Test-Simulation Comparison
Injury Criteria | Limit | Test (A05065) | Simulation
HIC | 1000 | 537 | 770
Upper Neck Tension (lb) | 405 | 140 | 213
Upper Neck Compression (lb) | 405 | 162 | 152
Upper Neck Shear (lb) | 186 | 103 | 117
Upper Neck Torque (in-lb) | 1018 | 141 | 99
Upper Rib Deflection (in) | 1.73 | 1.1 | 0.70
Middle Rib Deflection (in) | 1.73 | 0.75 | 0.50
Lower Rib Deflection (in) | 1.73 | 0.55 | 0.32
Abdominal Forces (lb) | 562 | 45 | 134
Pubic Symphysis Force (lb) | 1350 | 203 | 748
Shoulder Strap Load (lb) | 1750 | 41 | 333

## Slide 17: Test-Simulation Comparison
Injury Criteria | Limit | Test (A05065) | Simulation
HIC | 1000 | 537 | 770
Upper Neck Tension (lb) | 405 | 140 | 213
Upper Neck Compression (lb) | 405 | 162 | 152
Upper Neck Shear (lb) | 186 | 103 | 117
Upper Neck Torque (in-lb) | 1018 | 141 | 99
Upper Rib Deflection (in) | 1.73 | 1.1 | 0.70
Middle Rib Deflection (in) | 1.73 | 0.75 | 0.50
Lower Rib Deflection (in) | 1.73 | 0.55 | 0.32
Abdominal Forces (lb) | 562 | 45 | 134
Pubic Symphysis Force (lb) | 1350 | 203 | 748
Shoulder Strap Load (lb) | 1750 | 41 | 333

## Slide 18: Head Acceleration

## Slide 19: Head Contact
HIC is higher in simulation (770 vs. 537)
Head resultant has lower peak but wider duration
  HIC duration: test Δt = 6.4, simulation Δt = 19.4
Similar energy, softer contact in simulation
  1” difference in wall placement also a factor

## Slide 20: Thorax Contact
Thorax interaction with wall different between test and simulation
Test: Arm is trapped between body and wall
  Reduces loads (ATD and strap)
  Increases deflections
Simulation: Shoulder rotates in front of ribs
  Peak loads (ATD and strap) and deflections occur at or before shoulder rotation

## Slide 21: Shoulder Interaction

## Slide 22: Pelvic Contact
Pubic Symphysis Force much higher
  748 lb vs. 203 lb
Cause uncertain
  May be related to simplified seat bottom cushion representation
  No pelvic contact with wall
Value still half the injury limit

## Slide 23: Point Comparison
The v-ATD to wall interaction is similar to the physical ATD to wall interaction from an injury criteria perspective
Mostly conservative
Simulation appears to be sufficient to show trends

## Slide 24: Simulation Results: Shoulder Strap
Injury Criteria | 90° | 75° | 60° | 45° | 30°
HIC | 770 | 673 | 529 | 349 | 160
Upper Neck Tension (lb) | 213 | 193 | 189 | 253 | 260
Upper Neck Compression (lb) | 152 | 141 | 151 | 114 | 66
Upper Neck Shear (lb) | 117 | 90 | 66 | 62 | 33
Upper Neck Torque (in-lb) | 99 | 147 | 133 | 87 | 139
Upper Rib Deflection (in) | 0.70 | 0.63 | 0.32 | 0.15 | 0.13
Middle Rib Deflection (in) | 0.50 | 0.46 | 0.28 | 0.15 | 0.10
Lower Rib Deflection (in) | 0.32 | 0.34 | 0.27 | 0.11 | 0.05
Abdominal Forces (lb) | 134 | 85 | 84 | 69 | 197
Pubic Symphysis Force (lb) | 748 | 868 | 798 | 937 | 1004
Shoulder Strap Load (lb) | 333 | 434 | 557 | 804 | 930

## Slide 25: Shoulder Strap, 45° Simulation

## Slide 26: Rib Deflections (With Shoulder Strap)

## Slide 27: Simulation Results: No Shoulder Strap
Injury Criteria | 90° | 75° | 60° | 45° | 30°
HIC | 858 | 758 | 677 | 533 | 427
Upper Neck Tension (lb) | 140 | 179 | 175 | 319 | 353
Upper Neck Compression (lb) | 204 | 351 | 296 | 261 | 121
Upper Neck Shear (lb) | 120 | 106 | 88 | 64 | 57
Upper Neck Torque (in-lb) | 399 | 177 | 188 | 134 | 147
Upper Rib Deflection (in) | 1.13 | 0.88 | 0.61 | 0.41 | 0.15
Middle Rib Deflection (in) | 0.56 | 0.47 | 0.39 | 0.19 | 0.08
Lower Rib Deflection (in) | 0.35 | 0.28 | 0.22 | 0.06 | 0.06
Abdominal Forces (lb) | 230 | 149 | 229 | 186 | 170
Pubic Symphysis Force (lb) | 782 | 853 | 1017 | 1634 | 1923
Values in red exceed injury criteria limit

## Slide 28: HIC

## Slide 29: Upper Neck Tension

## Slide 30: No Shoulder Strap, 30° Simulation

## Slide 31: No Shoulder Strap, 30° Simulation

## Slide 32: Conclusions (1)
When seated next to a padded full wall with an effective shoulder restraint and body-centered lap belt, the ES-2re v-ATD suggests that the injury criteria listed in PS-ANM-25-03-R1 are unlikely to be exceeded for any angle between 30° and 90°
  More forward-facing angles are also unlikely to exceed the side-facing specific injury criteria
The ES-2re appears to be capable of avoiding internal damage in this configuration

## Slide 33: Conclusions (2)
Simulations without a shoulder restraint suggests that the ES-2re v-ATD is not capable of flailing in a realistic manner
  This configuration simulates an ineffective shoulder restraint
Internal damage to the ribs is likely to occur in this configuration

## Slide 34: Future Work
Additional evaluations are needed to evaluate configurations that allow more occupant flailing (e.g., armrest)
It is unknown what unique injuries can occur in oblique seats; therefore, the instrumentation requirements are also unknown

## Slide 35: Questions?