## Slide 1: Head Injury Criterion for Aviation Airbag Applications
The Seventh Triennial Fire & Cabin Safety Research Conference
Joseph A. Pellettiere, Chief Scientific and Technical Advisor for Crash Dynamics
December 2013

## Slide 2: Objective
Purpose: Develop appropriate evaluation criteria for inflatable restraint impacts
Compare HIC Unlimited with HIC 15
Evaluate Nij where applicable/available
Compare Hybrid II with FAA Hybrid III
Will review and summarize video and testing from several studies of interest

## Slide 3: Data Sources
Sled tests conducted as part of class demo
  Hybrid II with airbag
  2 FAA Hybrid III’s with airbags
Industry supplied data
  Compares HICu with HIC15
  Compares HICu with HIC15 and Hybrid II with FAA Hybrid III
CAMI research data
  Nij calculation for non-airbag tests

## Slide 4: Head Injury Criterion (HIC)
Resultant head acceleration
Calculated after contact
No limit on duration
<1000 represents ~ 23% risk of AIS 3+ (severe) head injury
Applied in multiple directions

## Slide 5: Neck Injury (Nij)
Tension
Compression
Flexion
Extension
Ntf
Ncf
Nce
Nte
No Injury
Nij=Fz/Fzc + My/Myc
Focused on frontal and rearward motion
No shear limits
No lateral bending limits
<1 represents ~20% risk of AIS3+ (severe) neck injury
Notes: Fzc = 6806 N (tension)
Fzc = 6160 N (compression)
Myc = 310 Nm (flexion)
Myc = 135 Nm (extension)
Ft = 4170 N
Fc = 4000 N

## Slide 6: FMVSS 208 changes
Hybrid III adoption
  Improved biofidelity
  Increase measurement capability
Limiting HIC window provides:
  Equally stringent evaluation for long durations, with decrease acceptance level
  Increased stringency for short durations, where biomechanical certainty is not as strong
Nij adopted to address
  Airbag loading
  Fatalities to children

## Slide 7: Data Summary
2 Class Demo tests
Part 23 Crew data
Industry supplied Part 25 data
CAMI research test data

## Slide 8: 16 G 44 ft/s

## Slide 9
Left Side Occupant Head Impact (Hybrid-II)
Air Bag Contact

## Slide 10: Hybrid II Airbag Contact
Notes: Both passed, case where lower acceptance value of HIC 15 does not make it a fail!

## Slide 11: Planned Test
16G, 44 ft/sec
Business class double
Hybrid II in front seat
FAA Hybrid III in launch seat
Barrier bag
Wedge bag

## Slide 12: Barrier Bag

## Slide 13: ATD Contacts- Left

## Slide 14: Wedge Bag

## Slide 15: ATD Contacts- Right

## Slide 16: Left ATD HIC
No contact with fwd seat back
HIC: 693.3
T1= 129.7 ms
T2= 210.8 ms
HIC15: 306
T1=150.9 ms
T2=165.9 ms

## Slide 17: Left ATD Upper Neck
Forces Moments
Nij =.46 @ 0.152

## Slide 18: Right ATD HIC
Contact with fwd seat back
HIC: 400.4
T1= 140.9 ms
T2= 156.0 ms
HIC15: 400.4
T1=140.9 ms
T2=155.9 ms

## Slide 19: Right ATD Upper Neck
Forces Moments
Nij =.85 @ 0.155

## Slide 20: Planned test summary
Only minor contact with inflatable restraint
HIC15 lower than HICu
All HICs passed
All Nij passed

## Slide 21: HII vs. FAA HIII
Rigid Fixture
3 pt. Belt, Wedge bag
No head contact with wall
Part 23 crew (26G)
Neck data not collected
 |  | Hybrid II |  |  | FAA Hybrid III |  | 
 |  |  | T1 | T2 |  | T1 | T2
HICu | Test1 | 1339 | 74 | 186 | 844 | 67 | 203
 | Test2 | 1294 | 73 | 193 | 1131 | 71 | 200
HIC15 | Test1 | 486 | 102 | 117 | 406 | 102 | 117
 | Test2 | 514 | 103 | 118 | 430 | 101 | 116
130 ms duration
Notes: HIC15 now passes where HICu fails, also note long duration of HICu window

## Slide 22: HICu vs. HIC15
Test | HICu | HIC15
B1 | 1029 | 622
B2 | 1303 | 582
C1 | 1032 | 812
C2 | 1008 | 822
F1 | 1106 | 893
F2 | 1020 | 943
F3 | 1346 | 1186
F4 | 1174 | 864
Industry data
Non-airbag tests
Double peaks
HIC15 significantly lower
HIC15 generally chose first peak
2 cases where HIC15 < 700

## Slide 23: HICu vs. HIC15
HICu: 1029
HIC15: 622
HICu: 1020
HIC15: 943
Note: HICu includes both peaks together

## Slide 24: Forward Facing Seat Nij*
Chart: 
| 4-Pt | 4-Pt | 4-Pt | Lap | Lap | Lap | Lap | Lap | Lap | Lap | Lap | Lap | Lap | Lap
Series 1 | 0.55 | 0.54 | 0.58 | 0.85 | 0.77 | 0.8 | 1.06 | 0.67 | 0.77 | 0.83 | 0.76 | 0.77 | 0.76 | 0.9
No Contact
Torso
Contact
Seat Back
Dbl
Row
Wall
Wall &
Ledge
* DeWeese R, Assessment of Head and Neck Injury Potential for Occupants of Typical Aircraft Seats and Interior Configurations During Forward Impacts,Fifth Triennial International Aviation Fire and Cabin Safety Research Conference

## Slide 25: Possible Solution
Modify HIC and use FAA Hybrid III with Neck Loads
Use HIC15 < 700
  Simple definition of contact, algorithm was able to calculate start/end times
  Generally takes only the first peak
Incorporate Nij <1 from FMVSS 208
Seats generally do not fail Nij
Notes: No need to define when the “soft” contact ocurrs with the airbag

## Slide 26: HIC 15
Use would eliminate failure from “lower” g longer duration contacts that would be typical of inflatables
Consistent with transition to HIC 15 in FMVSS 208
Limitation is if a secondary contact with a hard structure after an inflatable contact?

## Slide 27: Conclusions
HIC15 good for airbag contacts
  Start usually after contact, good when you have soft contacts making it difficult to determine start
Nij only exceeded when HIC was also exceeded
In this series FAA Hybrid III generally had lower HIC values
  More pronounced with HICu vs. HIC15
Additional data to be collected and welcomed