## Slide 1: Lithium Battery Systems for Aerospace Applications
8th Triennial Fire and Cabin Safety Conference
Fire Safety Conference
Norman Pereira
Oct XX, 2016

## Slide 2: Outline
Provide awareness of benefits and considerations associated with installing lithium battery and battery systems
  Aircraft manufacturers and operators are incorporating lithium battery technology at a rapid pace
Mitigations promoting safe installation of lithium batteries and battery systems in aircraft

## Slide 3: Background
Benefits from using lithium technology:
  Significant weight reduction
  High energy storage capabilities
  Reduced maintenance intervals
lithium batteries and battery systems have certain airworthiness considerations
As with any relatively new technology, we continue to learn more about the performance characteristics of both rechargeable and non-rechargeable lithium batteries

## Slide 4: Lithium Batteries
Examples of lithium batteries and battery systems:
  Cockpit displays
  Brakes
  Emergency batteries (e.g., EXIT signs)
  Emergency lighting
  Seat belt systems
  Underwater Locater Beacons
  Emergency Locater Transmitters (ELT)

## Slide 5: Potential Issues
Overcharging:
  In general, rechargeable lithium batteries have different internal failure causes than nickel-cadmium or lead-acid batteries
    Thermal runaway: earlier lithium batteries could be overcharged and result in uncontrolled increase in temperature and pressure
    Can result in overcharging of internal cell components
  Battery capacity, not just size, should be considered due to the higher amount of electrolyte and energy

## Slide 6: Potential Issues continued
Over-discharging:
  Discharge of some types of these batteries beyond a certain voltage (typically 2.4 volts) can cause corrosion of the electrodes in the cells
  For Rechargeable Lithium batteries, recharging a damaged battery or battery system can lead to an uncontrollable exothermic reaction
    Corroded electrodes become a source of short circuit and may result in a chemical reaction between the electrolyte and the solvent
    This may result in an uncontrolled increase in temperature and pressure

## Slide 7: Potential Issues continued
Internal Short Circuit:
  Internal Short Circuit could be due to many attributes including but not limited to the following:
    Manufacturing Defects
    Impurities
    Foreign Object Deposits
  This may result in uncontrolled increase in temperature and pressure leading to a thermal runaway
Reverse Charge or Back Charge in Non-Rechargeable Lithium batteries:
  This is a possibility for a non-rechargeable battery of more than one cell.
  This may also lead to a thermal runaway.

## Slide 8: 14 CFR Battery Regulations & Standards
§23.1353 Storage battery design and installation
§25.1353 Electrical equipment and installations
§27.1353 Storage battery design and installation
§29.1353 Electrical equipment and installations
Technical Standard Orders
  For non-rechargeable lithium batteries
    TSO-C142a (MOPS using RTCA/DO-227)
  For rechargeable lithium batteries
    TSO-C179a (MOPS using RTCA/DO-311)

## Slide 9: Mitigation of Lithium Battery Issues
Special Conditions
  Policy Statement for part 23/25/27 and 29.
    PS-AIR-20-130-02-01: Provides direction on the requirement and implementation for installation of rechargeable lithium batteries and battery systems
    This policy statement is located: http://www.airweb.faa.gov/
Means of Compliance (MOC) Issue Paper (IP) by the respective Directorate and Aircraft Certification Office
  Issue Paper addresses special condition
    AC 20-184 released on 15 October, 2015.
    RTCA/DO-311,DO-347 and DO-227: design, testing, and validation criteria
  Special conditions used in conjunction with existing regulations

## Slide 10: Lithium Battery Safety Considerations
Examples of tests and validations used to mitigate issues presented in previous slides for rechargeable lithium batteries:
  Short Circuit Test of a cell
  Short Circuit Test with Protection enabled/disabled
  Deep Discharge Test
  Overcharge Test with Protection enabled/disabled
  Thermal Runaway Containment Test

## Slide 11: Upcoming FAA Guidance
Documents currently in development:
  Update to Industry Standard RTCA/DO-311 (planned Dec 2016)
    Update to TSO-C179a (planned September 2017)
    Update to AC 20-184 using RTCA/DO-311A as a means to provide guidance on certification of rechargeable lithium batteries on aircraft (planned September 2017).
  Update to industry standard RTCA DO-227 (planned June 2017)
    Update to TSO-C142a (planned September 2017)
    A new AC to using RTCA/DO-227A as a means to provide guidance on certification of non-rechargeable lithium batteries on aircraft (planned September 2018)

## Slide 12: Lithium Battery Systems for Aerospace Applications
Questions

## Slide 13: FAA Battery Policy Contact
Norman Pereira - AIR133
Telephone Number: (202) 267-1639
Email: norman.pereira@faa.gov