## Slide 1: Improvements in Aircraft Smoke Detection
Presented to: 9th Triennial International Aircraft Fire and Cabin Safety Research Conference
By: Jennifer Wood
Date: October 30, 2019

## Slide 2: Introduction
Flight detection systems must provide a visual indication to flight crew within one minute of fire starting [1]
Minimum Performance Standards issued by FAA to decrease the frequency of nuisance alarms, e.g.
  Dust
  Water vapor/humidity
  Insecticides
Prior research by Chin: high proportion of smoke detector activations due to non-fire sources [2]

## Slide 3: Background
Fires & false alarms lead to:
  Flight diversions
  Flight delays
  Flight cancellations
  Emergency evacuations
  Lack of trust in systems (false alarms)
2014 database proved nuisance alarms made up 91.3% of reported incidents inside of cargo compartments

## Slide 4: Background cont.
Scalability of Smoke Density and the Viability of New Detection Methods in Aircrafts Research by Chin
  ASD outperformed the wired detector in response time
  Blue & IR wavelength and gas sensor technology responded well in comparison to light obscuration
  Wireless detectors proposed

## Slide 5: Objective
Address the ability of state-of-the-art (S-O-A) detectors and detection systems
  Blue & IR sensors
  Gas sensors
  Wired and Wireless Detectors
Assess differences in fire detection time for detectors within a ULD versus a cargo compartment ceiling
Further exploration of nuisance source testing
Ongoing project

## Slide 6: Current Technologies
Smoke detectors most commonly used in cargo compartments
    Often found on ceiling of cargo compartment
      Draw-Through Type (Air Sampling Port) OR
      Open-Area Type (Single Unit)
    Photoelectric sensing
Notes: Analyzing the hazard of Lithium Ion batteries
Blue whirl – using a fire tornado that generates a minimal amount of soot to remediate oil spills by burning without air pollution
Understanding sprinkler sprays to alter last century’s design methods using state-of-the-art diagnostics
Fire detection on aircraft – developing new technologies to reliably detect fires (without false alarms) in cargo compartments
Wildland fires – developing improved fire simulations to better predict the spread of wildland fires
New materials research – developing next generation fire retardants which are effective and environmentally friendly

## Slide 7: Experimental Program
Experiments conducted in Summer 2019 at the FAA Technical Center
Testing performed inside cargo compartment of DC-10

## Slide 8: Testing: Unit Loading Device (ULD)
Account for wide variety of ULD shapes & sizes, used 3 different leakage models
  “small” leakage = no alterations, all holes sealed
  “medium” leakage = only edge column of holes sealed
  “large” leakage = both columns of holes open
  CO2 leakage rate test results:
LD3 ULD Model | Leakage Rate (cfm)
Small Leak | 3.6
Medium Leak | 5.4
Large Leak | 9.1
Hole Columns

## Slide 9: Instrumentation
# | Instrument | Description/Measurement | Quantity
1 | Light Obscuration Meters | amount of white light transmitted through the smoke received by a photocell | 6
2 | Gas Analyzers | concentration of carbon monoxide, carbon dioxide, and oxygen. | 4 Sampling Points
3 | Thermocouples (K-type) | temperature at single points, placed at ceiling level and on trees. | 45
4 | Infrared (IR) Camera | amount of heat emitting from a certain area to create “thermal image” | 1
5 | Scanning Mobility Particle Sizer Spectrometer (SMPS) | density, diameter, and size distribution of airborne submicron particles. | 1

## Slide 10: Instrumentation
# | Instrument | Description/Measurement | Quantity
6 | Blue & IR Signal | light transmission in specific wavelengths using blue and IR signals (signals indicate prevalence of small (< 1 m) or large particles in smoke) | 1
7 | Air Sampling Detectors (ASD) | ASGD measures concentration of gases at selected positions through air sampling pipes, similarly to an ASSD which works as a smoke detector | 3 sampling ports/3 different systems
8 | Wireless Smoke Detectors | Photoelectric smoke detector using a wireless transmission system powered by batteries. | 2
9 | Wired Smoke Detector | Photoelectric smoke detector with hard wired power supply | 1
10 | GoPro | Video recording camera to document test conditions | 2

## Slide 11: Test Set Up: Cargo Compartment

## Slide 12: Test Set Up: Inside of ULD

## Slide 13: Test Set Up: Implementation
Inside ULD
Cargo Compartment

## Slide 14: Fuels & Test Matrix
Source/Location | Small Leakage Model | Medium Leakage Model | Large Leakage Model
PU Foam (flaming) | 3.0 by 3.0 by 2.0 in. burned 4” off the ground, near 100 g of foam Use of 4 mL of heptane to assist ignition (poured in corner) Ignite corner |  | 
PU Foam (smoldering) | 100 g of foam, cut into pieces varying near 1 x 1 x 1.5 inches Foam on hot plate at a constant temperature ranging between 400-600 °F |  | 
Suitcase (whole suitcase) | Entire suitcase standing up, filled with 10 cotton XL cotton t-shirts Smoldering induced via electric charcoal starter at 550 W |  | 
Shredded Paper | Paper strips approximately 6 – 10 mm in width by 25.4 – 102 mm in length Shredded paper consisted of a mix of 20 lb paper and cardstock 42.6 g (1.5 oz) tamped down in 1’ tall metal tube with 1”x1” flue space in center. Tube placed on a 11.75” high ring stand and ignited via an 8” Bunsen burner with 6” flame. |  | 
Wood | 100 g of hickory wood chips Wood chips on propane burner at constant temperature ranging between 400-600 °F |  | 
Baled Cotton | 15 g of cotton Cotton on hot plate at a constant temperature ranging between 400-600 °F |  | 
Lithium Ion Battery | Place four Lithium Ion Batteries inside sealed pipe cage with a single hole at top Use a cartridge heater to force thermal runaway |  | 
Humidifier | Release water humidifier into air for 30 min. until ULD reaches a light obscuration < 60% |  | 

## Slide 15: Cargo Compartment view of ULD
60 seconds
120 seconds

## Slide 16: Cargo Compartment view of ULD
180 seconds
240 seconds

## Slide 17: Cargo Compartment view of ULD
300 seconds
360 seconds

## Slide 18: Cargo Compartment view of ULD
420 seconds

## Slide 19: Preliminary Results – Smoldering PU Foam

## Slide 20: Preliminary Results – Smoldering PU Foam
Chart: Detector Times versus Light Obscuration
Wireless Detector-ULD | 0 | 0 | 10
ASGD-ULD | 0 | 0 | 10
ASGD-CC | 0 | 0 | 10
Wireless Detector -ULD
ASSD-ULD

## Slide 21: Future Analysis
Continuation of converting the raw data
Comparison between measurement points
  1st Stage: Comparison of all measurements with light obscuration meter
  2nd Stage: Analysis of Stage 1 results and comparison between:
    Blue + IR signals
    Gas analyzers
    SMPS data: particle size & density
    Different ULD leakage models

## Slide 22: Computer Simulations
Fire Dynamic Simulator (FDS): recreate test scenario
    Fire characteristics
    Surrounding environmental characteristics
    Geometric variations in cargo compartment
    Models presence of other ULDs

## Slide 23: Acknowledgements
Federal Aviation Administration
  Robert I. Ochs, PhD
  Engineering Team
  Technicians
Selena Chin’s Research & Thesis
Academic Advisor: Dr. Milke
Undergraduate Assistants: Emily James and Adam Lee
Space Age Electronics
Xtralis (by Honeywell)

## Slide 24: Thank You!
Questions?
  Contact: Jennifer Wood
  Fire Protection Engineering Graduate Student,
  University of Maryland College Park
  Email: jenniferwood2211@gmail.com