## Slide 1: A Data Set for Calibrating the ES-2re Virtual Anthropomorphic Test Device for Aviation Configurations
FAA Triennial Fire and Cabin Safety Conference
David Moorcroft
October, 2019

## Slide 2: Background
FAA PS-ANM-25-03-R1 defines the technical criteria for approving side-facing seats
  Requires the use of the ES-2re for the injury criteria test
  49 CFR 572 Subpart U

## Slide 3: ES-2re Injury Criteria (1)
Head: HIC < 1000
Upper Neck Tension Force < 405 lb
Upper Neck Compressive Force < 405 lb
Upper Neck Torque (x-axis) < 1018 in-lb
Upper Neck Shear < 186 lb
Upper Torso Strap Load < 1750 lb

## Slide 4: ES-2re Injury Criteria (2)
Upper, Middle, Lower Rib Deflection < 1.73 inch
Sum(Front+Middle+Rear) Abdominal Force < 562 lb
Pubic Symphysis Force < 1350 lb
Lower Leg Flail Limit (35°)
Restraints Must Remain on ATD
Occupant Support Criteria

## Slide 5: Background
Physical Anthropomorphic Test Devices (ATD) must meet certain requirements which include calibration tests.
Notes: Overall height, weight, segment dimensions and weights, component tests, etc.

## Slide 6: Background
FAA allows for the use of modeling and simulation to demonstrate compliance with federal regulations in certain scenarios [Advisory Circular 20-146A]
Need for an accurate representation of the virtual Anthropomorphic Test Devices (v-ATD)
SAE ARP 5765A defines a methodology for calibrating a v-ATD
  Currently Hybrid II and FAA Hybrid III only
  Rev B to include ES-2re

## Slide 7: v-ATD Requirements [ARP 5765A]
Meet the requirements of the physical ATD geometry, mass distribution, joint locations, sensor locations, etc.
Sub-Assembly Evaluation
Pelvis Shape Evaluation
Dynamic Response Evaluation
  Evaluates loading conditions not covered by the other evaluations
Notes: General meaning it applies to all ATDs and was previously defined for the H2 + H3

## Slide 8: ES-2re Requirements
Defined by 49 CFR Part 572 subpart U
  159.6 ± 2.6 lb, 35.8 ± 0.4 inch sitting height
Sub-Assembly Evaluations
  572.182 Head
  572.183 Neck [low speed]
  572.184 Shoulder
  572.185 Thorax
  572.186 Abdomen
  572.187 Lumbar Spine
  572.188 Pelvis
Notes: 7 sub-assembly tests

## Slide 9: ES-2re Requirements
Dynamic Response Evaluation [Proposed]
  Evaluate neck tension close to injury limit (405 lb), shoulder belt interaction, and leg flail (35° limit)
  Two test conditions considered
    Rigid seat, 3-pt harness, with and without a half-wall/armrest
    9G sled peak selected to produce neck tension ~405 lb
    Teflon on seat pan and floor to limit friction
      Teflon was used in the Hybrid II and FAA Hybrid III tests
    Minimum three (3) repetitions

## Slide 10: Test Conditions [160.8 lb]

## Slide 11: Video (With Armrest)

## Slide 12: Video (No Armrest)

## Slide 13: Test Summary
Test # | Armrest | Sled Peak G | Velocity (ft/s) | Neck Tension (lb) | Sh Belt Load (lb) | Belt Payout (in)
A16044 | Yes | 9.2 | 26.9 | 395 | 1292 | 1.0
A16045 | Yes | 9.2 | 26.8 | 400 | 1369 | 1.0
A16046 | Yes | 9.3 | 26.6 | 393 | 1377 | 0.6
A16047 | No | 9.4 | 26.6 | 432 | 1364 | 0.4
A16048 | No | 9.4 | 26.5 | 395 | 1338 | 0.9
A16049 | No | 9.4 | 26.8 | 397 | 1372 | 0.8
A16050 | No | 9.3 | 26.8 | 423 | 1380 | 0.6
Avg |  |  |  | 405 | 1342 | 
St Dev |  |  |  | 16 | 40 | 

## Slide 14: ARP Channel List [Proposed]
Sled Ax | Shoulder Belt Load
Neck Tension | Right Lap Belt Load
Neck Shear (Fx, Fy) | Center Lap Belt Load
Neck Mx | Belt Payout
Neck My | Wall Load
Neck Mz | Leg Rotation
Blue text denotes primary channel
Black text denotes secondary channel
Notes: 12 channels

## Slide 15: Error Calculations
Error calculations follow the method defined in SAE ARP 5765A (except #4)
  Magnitude error = relative error on the peak
  Shape error = Sprague and Geers comprehensive error
  All calculations from 0 ms – 400 ms (by default)
  Calculated with 1k data

## Slide 16: Test Repeatability: Neck Fz
Max Mag Error: 2%
Max Shape Error: 5%
Max Mag Error: 9%
Max Shape Error: 6%
Notes: 44-45: mag error 0.9%, shape 2.6%
44-46: mag error 0.8%, shape 3.1%
45-46: mag error 1.7%, shape 5.1%
47-48: mag error 8.8%, shape 5.9%

## Slide 17: Test Repeatability: Neck Shear
Max Mag Error: 4%
Max Shape Error: 5%
Max Mag Error: 3%
Max Shape Error: 5%
Notes: 45-46: mag error 3.8%, shape 4.6%
47-48: mag error 2.5%, shape 5.1%

## Slide 18: Test Repeatability: Neck Mx
Max Mag Error: 4%
Max Shape Error: 4%
Max Mag Error: 10%
Max Shape Error: 9%
Notes: 44-46: mag error 3.6%, shape 3.8%
47-49: mag error 10.2%, shape 8.6%

## Slide 19: Test Repeatability: Sh. Belt Load
Max Mag Error: 7%
Max Shape Error: 5%
Max Mag Error: 7%
Max Shape Error: 5%
Notes: 44-46: mag error 6.6%, shape 5.1%
49-50: mag error 6.7%, shape 5.45%

## Slide 20: Test Repeatability: Wall Load
Max Mag Error: 14%
Max Shape Error: 17%
Pubic symphysis force also shows double spike, max load is 252 lbs
Notes: 44-45: mag error 14.0%, shape 14.8%
44-46: mag error 4.2%, shape 17.1%
Abdomen force < 50 lbs each
Pubic Symphysis force 210 lbs for A16044

## Slide 21: Discussion
Preliminary photometric analysis contains a geometrical error that will be corrected
  Data will not be included in full package until the error is corrected
Leg flail can be addressed via other means

## Slide 22: Leg Flail
ES-2re demonstrates poor coupling between torque and the amount of rotation
Angle limit is essentially a go/no-go evaluation of the mitigation strategy

## Slide 23: Leg Flail
Leg flail could be evaluated qualitatively as long as the leg freely flails beyond 35°
Model courtesy of Dynamore
Notes: For physical ATD going 80 degrees, flail of 70 degrees or 90 degrees is good enough .
Replace picture with gif?

## Slide 24: Leg Flail
Alternate quantitative data source is available
  Robert D. Huculak & Hamid M. Lankarani (2015) Methods of evaluating ES-2 leg flail in dynamic evaluation and certification tests of side-facing aircraft seats, International Journal of Crashworthiness, 20:6, 613-628, DOI: 10.1080/13588265.2015.1076586

## Slide 25: Test Repeatability: Head Rx

## Slide 26: Range of Impact Angles
The data included in this test series is only intended to evaluate the ES-2re during pure lateral loading
Extrapolation to the standard test conditions of ±10° yaw should be evaluated during system level validation
Physical testing of the ES-2re beyond 65° is not recommended
  Per Humanetics communication

## Slide 27: Data Set
A data set package will be made available to anyone interested
  Pre-test pictures and measurements
  Post-test pictures
  Electronic data
  Videos
May be posted to the SAE SEAT committee webpage to support ARP 5765 Rev B

## Slide 28: Summary
Full scale dynamic test conditions to evaluate the ES-2re v-ATD have been defined
Test data shows good repeatability (generally <10% variability)
A data package will be available to any interested party
Initial work by v-ATD developers shows good correlation between the v-ATD and physical ATD

## Slide 29: Acknowledgements
Thanks to the Biodynamics Team for running the sled tests: David Moorcroft, Amanda Taylor, Jeff Ashmore, Ronnie Minnick, David DeSelms (retired), Jim Biegler (contractor)
Restraints provided by AmSafe Corp. Commercial Aviation
A report containing the details of this project will be published as an Office of Aviation Medicine Report