## Slide 1: Narrow-body & Wide-body Mishap Kinematics Study
Lance C. Labun
John (Jack) P. Cress
Dale Kennedy
9th Triennial International Aircraft Fire & Cabin Safety Research Conference
October 28-31, 2019
Notes: Primary purpose of this presentation is to make the audience aware that his work has done and data been collected.

## Slide 2: Study Objectives
Quantify the kinematics of potentially survivable mishaps
Quantify the damage outcomes of mishaps
Quantify the injury outcomes of mishaps
Correlate outcomes to kinematics
Identify trends in outcomes
Add to the knowledge developed in the ditching regional jet study
Notes: Overall incentive is to understand the crashworthiness behavior of metal airframes to establish performance expectations for composite airframes.
To attempt to quantify what properties have contributed to crashworthiness in metal airframes.

## Slide 3: Mishap Selection Criteria
Mishaps of single aisle and multiple aisle commercial transport aircraft
Mishaps that were considered to be potentially survivable.
Mishaps for which detailed investigations were conducted and the reports were readily obtainable. Result: All western built airframes
86 narrow-body & 29 wide-body mishaps
N-B 1975-2014 W-B 1971-2014
Notes: Narrow body and wide body aircraft were the study charter
Mishaps for which there was no chance of survival were not of interest.
Time period covered is over 40 years. Definite evolution of investigation and report techniques and completeness.
More reports available from outside US and Europe as time progressed.

## Slide 4: Data Extracted
Aircraft type, engine configuration, # of seats, # of occupants
Kinematics: speeds, angles, accelerations
Aircraft damage: skin, floor, seats, fuselage breaks, survivable volume, by segment
Aircraft conditions: landing gear status, fire
Occupants & seats: # & location by segment
Injuries: minor/none, serious, fatal
Evacuation: functionality & usability of portals
Notes: All turbojets, all low wing, engine configuration is essentially engine location.
Numbers of seats and occupants by segment is important to analyzing injury outcomes.
Injuries limited to three levels consistent across reports.
Portals = doors and “exits”

## Slide 5: Mishap Scenarios
Data for both aircraft types broken down into “Mishap Scenarios” for additional analysis
  Runway overruns
  Compromised landing, remained on or near runway (gear up, gear collapsed, tail strike)
  Terrain contact short of runway during landing (tracked with or without localized wind influence)
  Landing on runway with loss of control
  Loss of control on take-off or go around (tracked with or without localized wind influence)
Notes: Scenarios each had distinctive characteristics
In an earlier study, looking at outcome as a function of the scenario was beneficial
“Localized wind influence” is wind shear

## Slide 6: Analysis
Notes: Having collected the data from the database, the data were transferred from the database queries into MS Excel worksheets.
The worksheets enabled data to be organized by different parameters and to used to converted to other units, calculated into metrics, ordered, plotted, and tabulated.

## Slide 7: Kinematics
Kinematics of the mishap impact
Airspeed, vertical velocity, flight path angle
Attitude angles at impact: pitch, roll, & yaw
Acceleration: longitudinal, vertical, lateral
Notes: In some cases these data had to be created using accident reconstruction techniques.
Most of the reconstructions were done by Jack Cress.
Some of these data were available from the flight data recorder, but the recording frequency was not sufficiently high to catch crash values.

## Slide 8: Aircraft Damage by Occupied Segment
Segments: Cockpit, forward cabin, overwing, aft cabin, tail (reflects break patterns)
Breaks between segments recorded (Y/N)
Underside skin damage (Widespread / Localized / None)
Floor disruption (W / L / N)
Seat failure (W / L / N)
Loss of occupant volume (W / L / N)
Combined to form a Damage Metric (0-112)
Notes: Survivability is strongly influenced by maintenance of a survivable volume and occupant retention.
Each type of damage is weighted according to its potential to contribute to severe injury and its quantity.
These are the damage types that were included in the damage metric and the levels that were recorded for each.
Floor disruption refers to floor buckling which potentially can lead to seat release.
Seat failure includes seat detachment regardless of whether the seat failed or the floor attachment.
Example: Seat failure widespread would imply that there were seat failures throughout the entire segment as opposed to a few seat failures in one area of the segment.
The range of values for the damage metric 0-112 for the entire aircraft, and 0-23 for each segment behind the cockpit.
Weighting: W=2x, L=1x, N=0x. Skin=1, Floor Disruption=2, Seat Failure = 3, Volume Loss =4, Break add 3 to the segment behind score.

## Slide 9: Occupant Injury
Injury severity: None/minor, serious, fatal
Occupants and their injuries were analyzed at the segment level
Injury fractions, (# of injuries/# of occupants) were correlated with: aircraft design, mishap scenario, kinematics, damage metric, external obstacles, and fire.
Binary logistical models were created to predict injury based on various parameters
Notes: Serious and fatal were often combined into “Severe injury” on basis that serious injuries were life changing events, rather than performing two analyses one for fatality and one for serious injury.
Binary logistical models were developed to provide predictive tools for severe injury fraction based on the various parameters.

## Slide 10: Evacuation
Fraction of mishaps with emergency evacuations
Fraction of doors and exits functional and usable
Also recorded the minimum number of portals usable
Notes: Evacuation is an important survival consideration in potentially survivable mishaps.
Beyond the occupant’s injuries, evacuation is critically dependent on the availability of escape portals
Fuselage breaks were not counted as escape portals, although they often became such. Some breaks did not result in large openings but did cause localized injuries.
The report contains information on the frequency of post-crash fire.

## Slide 11: Findings
Notes: Cannot possibly present all of the findings in a 20 minute presentation.
Encourage you to go to the report and study the parts of interest to you.

## Slide 12: Scenarios
 | Narrow-Body (percent of 86) | Wide-Body (percent of 29)
Runway Overrun | 30 | 24
Compromised Landing | 13 | 24
Impacted Short | 16 | 21
Impacted Short (Wind) | 6 | 7
Hard Landing Lost Control | 19 | 17
Lost Control TOGA | 8 | 7
Lost Control TOGA (Wind) | 8 | 0
Notes: Presenting the mix of scenarios.
Generally similar between the two aircraft types.
More overruns on the N-B
More compromised landings on the W-B

## Slide 13: Kinematics
Mean for all mishaps excluding overruns | Narrow-body (60 mishaps) | Wide-Body (22 mishaps)
Vertical Velocity (ft/s) | 22.3 | 22.2
Vertical Deceleration (G) | 3.9 | 4.0
Airspeed (ft/s) | 223 | 232
Long. Deceleration (G) | -3.5 | -2.8
Flight Path Angle (deg.) | -7.0 | -5.0
Pitch Angle (deg.) | +4.3 | +4.2
Notes: Overruns were excluded because they were generally lower in velocity and the outcome was sensitive to presence/absence of obstacles. Data and discussion of this is in the report.
Remarkably similar values for the two aircraft types.
Vertical velocities exceed the landing gear capability by a large margin

## Slide 14: Damage Metric Whole Aircraft
Mishap Scenario | Narrow Body (damage metric) | Wide Body (damage metric}
Runway Overrun | 22.0 | 13.9
Compromised Landing | 2.5 | 4.0
Impacted Short | 59.1 | 74.5
Impacted Short (wind) | 24.8 | 61.5
Hard Land. Lost Ctrl. | 10.1 | 36.4
Lost Ctrl. TOGA | 72.6 | 75.5
Lost Ctrl. TOGA (wind) | 55.1 | -
Notes: Remember the range for the metric is 0-112. A tail strike might lead to a 1. An impact short of the runway that severely damages the aircraft would be over 100.
Average whole aircraft damage metric for all mishaps in the scenario.
In terms of damage Impacting Short and Loss of Control during TOGA are the most severe scenarios.
Wind involvement appears to lead to less severe crashes in both impacting short and TOGA mishaps, no reason evident for this.
Wide-bodys experience greater damage in the severe scenarios.

## Slide 15: Severity of Injuries
 | Narrow Body (no. & %) | Wide Body (no. & %)
Fatal (all causes) | 1,818 (17.6 %) | 1,163 (16.9 %)
Fatal (reported as thermal) | 517 (5.0 %) | 373 (5.4 %)
Serious Injury | 788 (7.6 %) | 535 (7.8 %)
Minor or Not Injured | 7,704 (74.4%) | 5,213 (75.5%)
Total Occupants | 10,310 | 6,877
Notes: Overall injury rates are very similar for the two aircraft types.
Most occupants sustain only minor or no injuries.

## Slide 16: Severe Injury Percent by Scenario
 | Narrow Body (Severe Injury %) | Wide Body (Severe Injury %)
Runway Overrun | 20 | 7
Compromised Land. | 0 | 1
Impacted Short | 52 | 63
Impacted Short (wind) | 40 | 47
Hard Land. Lost Ctrl. | 8 | 24
Lost Ctrl. TOGA | 85 | 84
Lost Ctrl. TOGA (wind) | 48 | -
Notes: Severe Injuries are Fatalities plus Serious injuries
The same scenarios that experience high damage metrics, also experience high injury fractions

## Slide 17: Injury Fraction by Segment
Does not include Runway Overruns | Narrow Body (% severely injured) | Wide Body (% severely injured)
Cockpit | 40 | 50
Forward Cabin | 31 | 55
Overwing Cabin | 28 | 47
Aft Cabin | 23 | 36
Tail | 36 | 6
Notes: People ask where is the best place to sit.
No one area stands out as especially safe.
Avoid the likely break locations, yet cabin attendants tend to be behind cockpit or near tail break.

## Slide 18: Evacuation Results Overview
 | Narrow-body (# / # mishaps, percent) | Wide-body (# / # mishaps, [percent])
Emerg. Evacuation | 57/86 [66] | 20/29 [69]
Post-crash fire | 35/86 [41] | 17/29 [59]
Emerg. Evac. Fire a factor in Evac. | 35/57 [61] | 11/20 [55]
Notes: Importance of emergency evacuation planning.
Emergency evacuations occurred in over 2/3 of these mishaps.
There was post-crash fire present in more than 40 percent of the mishaps, higher for wide-body.
In more than half of the emergency evacuations, the occupants were ‘contending’ with presence of fire, i.e. number of portals reduced or access to some portals blocked.

## Slide 19: Escape Portals
 | Narrow-Body (Avg. # Rptd – Avg. # Usable) | Wide-Body (Avg. # Rptd – Avg. # Usable)
Overrun | 6.7 – 5.4 | 7.2 – 4.6
Compromised Ldg. | 4.7 – 4.2 | 8.0 – 4.3
Land Short (All) | 6.8 – 4.7 | 4.2 - 3.8
Hard Ldg. Loss of Ctrl | 7.2 – 5.6 | 5.0 – 4.3
TOGA (All) | 4.3 – 3.0 | 10.0 – 4.0
Notes: Narrow body 335 portals (doors + exits) usable of 444 reported. Wide body 109 doors usable of 196 reported.
Requiring that the evacuation test be run with half of the available portals is not overly conservative.

## Slide 20: Acknowledgments
Funded by Federal Aviation Administration
  Joseph Pellettierre & Alan Abramowitz
Funded through: National Institute for Aviation Research, Wichita State University
  John Tomblin
Report Status: Submitted to the FAA May 2018.
Report Title: Study of Transport Aircraft Water Mishap Kinematics and Regional Jet Mishap Kinematic
Notes: I would like to thank the FAA and in particular Joseph and Alan for soliciting and funding this work. And Dr. Tomblin for his participation in the funding of the work. The work was very satisfying to perform.