## Slide 1: Transport Aircraft Water Mishap Kinematics & Regional Jet Mishap Kinematics
Lance C. Labun
John (Jack) P. Cress
9th Triennial International Fire & Cabin Safety Research Conference
October 28-31, 2019
Notes: Paper is meant to make you aware of the existence of this report.
The report is too large to attempt presenting all of the results here.

## Slide 2: Study Objectives
Verify that the ditching requirements in existing regulations are consistent with the characteristics of recent mishaps wherein aircraft enter water
Quantify the kinematics of regional jet mishaps
Quantify the damage and injury outcomes of regional jet mishaps
Notes: The overarching purpose of both studies is to assure that the current regulations are suitable for defining crashworthiness and survivability of future aircraft.
The concept behind the term ‘ditching’ as addressed in the regulations appears to be that of an aircraft under-power and in control unable to reach a suitable landing strip and forced to put down in the sea. The crew and the passengers have time to prepare for the water impact and post-crash egress.

## Slide 3: Water Entry Mishaps

## Slide 4: Water Mishap Selection Criteria
All transport aircraft types
  Range of types: SD-360 to B747
Primary aircraft impact was with water
Final resting place of the aircraft was in water
Mishap was potentially survivable
A thorough investigation was conducted and the documentation was available
22 Mishaps included 1967-2013
Notes: Survivable mishaps only because the point of the study is to improve survivability and understand losses.
The requirement that a thorough investigation was conducted and documented was necessary to conduct the study, but that requirement also eliminated a lot of mishaps, and essentially eliminated eastern bloc manufactured aircraft.

## Slide 5: Water Mishap Data Extracted
Aircraft type & configuration
Kinematics: speeds, angles, accelerations
Damage: skin, floor, seats, fuselage breaks, survivable volume; by fuselage segment
Aircraft conditions: landing gear status, fire
Occupants & seats: # by segment
Injuries: minor/none, serious, fatal, drowning
Evacuation: functionality & usability of portals
Notes: Configuration included engine type, engine positons and wing high/low
Landing gear status: collapsed, not deployed
Drowning data were incomplete and could not be used conclusively

## Slide 6: Water Mishap Scenarios
Mishaps were assigned to a scenario for analysis
  Ditching with some thrust (3)
  Ditching without thrust (7)
  Landing on water short of the runway (5)
  Impact water during climb out (1)
  Runway overrun landing or takeoff (6)
Notes: Already here is a finding: There are more ditchings WITHOUT thrust than with thrust.
5 unplanned landings short of the runway. With thrust, but aircraft not being placed in the “ditching attitude,” AIRCRAFT ARE NOT PREPARED FOR WATER ENTRY, CABIN IS NOT PREPARED FOR WATER ENTRY
Only 3 of the 22 water entry mishaps are consistent with a ‘classic ditch’ scenario.
In all of the others one or more of the “resources” for survivability are missing. Thrust, control of impact attitude, cabin preparation.

## Slide 7: Analysis
Notes: Overview of how the analysis was conducted

## Slide 8: Aircraft Damage by Occupied Segment
Segments: Cockpit, forward cabin, overwing, aft cabin, tail (reflects break patterns)
Breaks between segments recorded (Y/N)
Underside skin damage (Widespread / Localized / None)
Floor disruption (W / L / N)
Seat failure (W / L / N)
Loss of occupant volume (W / L / N)
Combined to form a Damage Metric (0-112)
Notes: This slide describes how the aircraft damage was quantified.

## Slide 9: Occupant Injury
Injury severity: None/minor, serious, fatal
Occupants and their injuries were analyzed at the aircraft segment level
Injury fractions, (# of injuries/# of occupants) were correlated with: aircraft design, mishap scenario, kinematics, damage metric, external obstacles.
Binary logistical models were created to predict injury based on various parameters
Notes: Describes the types of analysis conducted on the injury data
Data analyzed at the aircraft segment level.

## Slide 10: Evacuation
Fraction of mishaps with emergency evacuations
Fraction of doors and exits functional and usable
Also recorded the minimum number of escape portals usable

## Slide 11: Findings
Notes: The report is 125 pages, so there is only time to present a few findings. The report is meant to be a design resource.

## Slide 12: Ditching with & without Thrust
 | Ditching with Thrust (3 mhps) | Ditching without Thrust (7 mshps)
Median Vertical Velocity (ft/s, – is downward) | -9.4 | -19.5
Median Airspeed (ft/s) | 148 | 187
Flight-path Angle (degrees, – is downward) | -3.6 | -7.0
Pitch angle (degrees , + is nose up) | 6.0 | 8.1
Impact Angle [Pitch Angle – Flight-path Angle] (degrees) | 9.8 | 15.1
Notes: Evident that the conditions for ditching without thrust are more “severe” than ditching with thrust.
Velocities both higher, vertical velocity substantially higher. Vertical KE is 4.3 x and Airspeed KE is 1.6x.
Steeper “impact angle” will lead to greater vertical velocity at nose. “Slapdown”

## Slide 13: Damage & Breaks by Scenario
 | Ditching with Thrust (Total Damage Metric / 2 Mishaps) {1 of 3 sank} | Ditching without Thrust (Total Damage Metric / 7 Mishaps)
Cockpit | 0 | 11
Forward Cabin | 0 | 9
Overwing Cabin | 6 | 5
Aft Cabin | 1 | 6
Tail | 0 | 7
# Fuselage Breaks / # Mishaps | 1 / 2 | 7 / 7
Notes: Damage is greater in mishaps occurring without thrust.
One ditching with thrust sank in deep water and was not recovered. The 15 of 24 damage fields could not be filled. The report noted that this aircraft “did not break up,” but little else was reported about the damage. No explanation for why it sank so quickly. A substantial fraction of occupants were lost in the sinking.

## Slide 14: Injuries by Segment
 | Ditching with Thrust (2) (Fatal + Severe Injury Percent) | Ditching without Thrust (7) (Fatal + Severe Injury Percent)
Cockpit | 0 | 60
Forward Cabin | 0 | 40
Overwing Cabin | 5 | 20
Aft Cabin | No occupants | 14
Tail | 100 | 88
Notes: Although ditchings with thrust have minimal data, the ditchings without thrust had higher rates of injury consistent with the higher damage and more frequent fuselage breaks. 1 of 3 with-thrust mishaps had incomplete data, i.e. the sinking

## Slide 15: Evacuation
Scenario | Doors Avg. # on Aircraft | Doors Avg. # Usable | Exits Avg. # on Aircraft | Exits Avg. # Usable
Ditching with Thrust | 1.67 | 0.33 | 2.67 | 2.50
Ditching without Thrust | 2.70 | 0.80 | 2.43 | 1.60
Landing Short of Runway | 4.20 | 2.20 | 4.00 | 2.80
Overrun | 6.0 | 3.8 | 2.66 | 2.00
Notes: Generally fewer portals are usable than available.
Ditching with Thrust generally resulted in more usable portals compared to ditching without thrust

## Slide 16: Regional jets

## Slide 17: Regional Jets
24 mishaps Time range: 1972-2010
Turbojet powered
Transport aircraft seating <100 (Avg = 66)
Small diameter fuselage, generally minimal underfloor space
Wt 12,500 to 100,000 lb as search criterion
Dominant design: low wing, 2 aft engines, 4-5 seats per row.
Notes: As the aircraft in this class have grown, the capacity has encroached on the low end of the “narrow-body” class such as the B737-100 and A318. Original “concept” a stretched biz jet. In fact a couple of larger chartered biz jet mishaps were included.

## Slide 18: Mishap Scenarios
Scenario | Mishaps (#) | Average Damage Metric for Mishaps
Runway Overrun | 8 | 7.8
Compromised Landing | 3 | 6.9
Impacted Terrain Short | 4 | 60.3
Hard Landing Lost Ctrl. | 3 | 12.6
Lost Control TOGA (Take-off or Go Around) | 6 | 73.8
Notes: Compromised landings included retracted gear, collapsing gear, & tail strikes.
Lost control TOGA events included several instances of contaminated wings. Pilots seemed unaware of how sensitive the wings were to contamination particularly in earlier mishaps.
TOGAs had worst outcomes as can be seen from the damage metric values.

## Slide 19: Injuries by Scenario & Segment
Scenario | Cockpit (% Severe) | Forward Cabin (% Severe | Overwing (% Severe) | Aft Cabin (% Severe) | Tail (% Severe)
Overrun | 14 | 2 | 2 | 2 | 25
Compro-mised Ldg | 0 | 0 | 0 | 0 | 0
Impact Short | 64 | I.D. | I.D. | I.D. | N.O.
Ldg Lost Control | 13 | 28 | 0 | 0 | N.O.
TOGA Lost Ctrl | 78 | 59 | 80 | 97 | 86
I.D. = Insufficient Data N.O. = No Occupants.
Notes: Percent of occupants in each segment receiving severe injury
In these small aircraft the cockpit is vulnerable, as is the tail.
Cabin attendant seats are often counted in the cockpit.

## Slide 20: Evacuation Portals
Scenario | Doors Avg. # on Aircraft | Doors Avg. # Usable | Exits Avg. # on Aircraft | Exits Avg. # Usable
Overrun | 2.38 | 1.57 | 1.75 | 1.13
Compro-mised Ldg | 3.33 | 3.00 | 3.00 | 2.00
Impact Short | 1.50 | 0.33 | 1.50 | 0.33
Landg Lost Control | 2.00 | 0.67 | 2.00 | 2.00
TOGA Lost Control | 1.67 | 0.33 | 2.67 | 0.25
Notes: Counts only intended portals, does not attempt to count fuselage breaks as potential exits.
Usable is both functional and usable to escape, i.e. no fire, slide or jump height
More severe scenarios have fewer usable portals.
Avg value <1 implies some mishaps had zero.
More detail in the report.

## Slide 21: Acknowledgments
Funded by Federal Aviation Administration
  Joseph Pellettierre & Alan Abramowitz
Funded through: National Institute for Aviation Research, Wichita State University
  John Tomblin,
Labun, L.C.; Cress, J.P.; STUDY OF TRANSPORT AIRCRAFT WATER MISHAP KINEMATICS AND REGIONAL JET MISHAP KINEMATICS; DOT/FAA/TC-17/52 for Federal Aviation Administration, October 2017.
Notes: Citation for the report.
I would like to thank the FAA and in particular Joseph and Alan for soliciting and funding this work.
And Dr. Tomblin for his participation in the funding of the work. The work was very satisfying to perform.