## Slide 1: Joint EUROCAE/SAE Hydrogen Fuel Cells Standardization Group WG-80/AE-7AFC
AIR7765 / ER-020
Considerations for
Hydrogen Fuel Cells
in Airborne Applications

## Slide 2: AIR 7765 / ER-020 Executive Summary
Objective
Introduction to Hydrogen
Hydrogen Usage
Hazards and Mitigations
Benefits for Airborne Applications
Conclusions

## Slide 3: Objective
Why to use hydrogen as an energy carrier
  Efficiently produce and store energy
  Water emissions only
  Key technology for energy security
Why and how to use hydrogen fuel cells in aviation
  Aviation environmental targets
  Efficient Hybrid-electric air vehicles
Experience with mobility sector transferable to aviation
    Alleviate safety concerns
    Demystify hydrogen for aviation

## Slide 4: Introduction to Hydrogen
Hydrogen Properties
  Gaseous in standard conditions
    Liquid @ -253°C/-423°F
  Colorless, odorless
  Non-toxic, non-polluting, not radioactive
  Lowest density gas with highest energy content by mass
  Has wide flammability range
  Has low ignition energy
  Has high self-ignition temperature
    Twice the jet fuel
  Flame burning characteristics (adiabatic)
    Different from jet fuel
      Lower temperature
      Lower radiation

## Slide 5: Introduction to Hydrogen
Production
  Generated by hydrocarbon reforming
    Mainly steam methane reforming
  Also produced through water electrolysis
Transportation and Storage
  Stored as gas in pressurized vessels or as liquid in cryo-tanks
  Transported by pipeline, truck, rail and ship
Distribution
  Daily distributed for various industries via dedicated and mature installations (e.g. refueling stations for cars, buses, forklifts, etc.)
Cost
  Fuel cost to car owner by range same as gasoline with hydrogen un-taxed
  More efficient fuel cells will balance future hydrogen taxes

## Slide 6: Introduction to Hydrogen
Public Perception has Changed
  Recognized safe use in industry processes (fertilizers, steel, electronics, etc.)
    Chemical and petrochemical industries safely deal with reactions with hydrogen
    This knowledge serves as base for safety in the hydrogen fuel cell sector
  Increasing usage in mobility (cars, buses, forklifts, etc.) with direct involvement of the general public
  Now seen as a key for low carbon energy systems to address climate change

## Slide 7: Hydrogen Usage
Hydrogen, known and used since 18th century
  1783 in balloons and blimps as lighter-than-air gas
  1830 for illumination and heating as city gas
  1960s in fuel cells for electricity – terrestrial vehicles and Gemini and Apollo missions
In fuel cells for mobility sector
  Bus, car, boat, train, tramway, truck, forklift, scooter, bicycle
    30,000 vehicles by 2018
    >80,000 expected by 2020
    >300,000 expected by 2025
  Civil drones

## Slide 8: Hydrogen Usage
Green energy source for residential and industrial applications
  Source of heat and electricity
    Remote locations benefit from independency from normal grid
    Government Programs:
      EneFarm (Japan) : 250,000 units in 2018
      Ene.field + PACE (Europe) : 3,500 units by 2021
  Megawatts power source plants as primary and backup for whole neighborhoods, buildings and industries
    South Korea and USA are major players

## Slide 9: Hydrogen Usage
Hydrogen Refueling Stations (HRS)
  325 HRS (for cars and buses) in operation worldwide in 2019
    Expected > 1000 HRS by 2025
    12,000 vehicles served daily
  Near 10,000 forklifts fueled daily in storehouses
  Introduction of HRS on airfields will be straightforward
    Demonstration projects conducted in several airports

## Slide 10: Hydrogen Usage
Hydrogen in the Energy Transition
  Central component for energy transition
  Proposed as the foundation of a sustainable low-carbon economy
  Contribute to Paris Agreement objectives against global warming
  May play 7 major roles*:
    Enabling large-scale renewable energy integration and power generation
    Distributing energy across sectors and regions
    Acting as a buffer to increase energy system resilience
    Decarbonizing transportation
    Decarbonizing industrial energy use
    Helping to decarbonize building heat and power
    Providing clean feedstock for industry
  Ambitious nation-wide initiatives already trigger Hydrogen economy
    Japan, South Korea, Germany, USA
*Hydrogen Council (https://hydrogencouncil.com/en/)

## Slide 11: Hazards and Mitigations
Fire Hazard
  Contrast with jet fuel storage
    Segregated from air
      No ignition risk inside the tank
    No need for tank inerting
    Overboard ventilation
    Purging/inerting for plumbing
    Centralized tanks
      Reduced number of zones prone to leakages
  Double wall for separation & segregation of leakages
  Explosion proof qualification for electric equipment
  Sensors
    Hydrogen Concentration
    Oxygen Concentration
    Fire Detection
      Optical
      Thermal

## Slide 12: Hazards and Mitigations
Explosion Hazard
  Prevent leakages
    Double wall concept
  Prevent accumulation
    Provided ventilation, purging and dump valves
Pressure Hazard
  Addressed as other pressurized vessels already used in airplanes
    Such as Oxygen, fire extinguishing, hydraulic accumulators, etc.
Liquid Hydrogen cryogenic (-253°C/-423°F) hazard
  Prevent leakages
    Double wall concept
  Insulation to mitigate contact with low temperatures surface
  Prevent trapping of LH2/pressure build up
    Overpressure relief devices
  Prevent embrittlement with proper materials

## Slide 13: Benefits for Airborne Applications
Benefits More Electric Airplanes (MEA)
Hydrogen as clean energy carrier
Better efficiency
  Reduction of fuel consumption
  Reduction of emissions
Fewer energy vectors on-board (electricity)
Usable by-products
  Heat for cabin and galleys
  Water for galleys and toilets
  Oxygen Depleted Air (ODA) as inerting for cargo and fuel tanks

## Slide 14: Conclusions
Proliferating electric vehicles
  Fuel cell vehicles
    Greater range than batteries
    Refueling time comparable to regular fuels
    #1 automotive trend
Significant benefits to fuel cells in aviation
  Hydrogen is safe to use
  Insights and lessons learned from other sectors will benefit aviation
Availability of hydrogen for ground mobility will reduce barriers for aviation
Key technology for upcoming more (and all) electric aircraft

## Slide 15: THANK YOU

## Slide 16: Joint EUROCAE/SAE Hydrogen Fuel Cells Standardization Group WG-80/AE-7AFC
Working Group Chairman
Olivier Savin
Dassault Aviation
olivier.savin@dassault-aviation.com