## Slide 1: Flow Visualization in the OSU
IAMFTFM
Tina Emami
March 5-6, 2019

## Slide 2: Airflow Project Goals
Create an adjustment to the current OSU apparatus in order to create an even and reproducible air flow.

## Slide 3
Measurement Location

## Slide 4: Measurement Location
The PIV camera is aligned to view the flow between the middle two glow bars

## Slide 5: New Test Setup
Air inlet was moved back to side inlet location
PVC tube with two rows of evenly spaced 5/8” holes 45° from horizontal was constructed
Cap is glued to the end of the tube
Tube is placed in the bottom chamber of the OSU
Holes will be oriented to face downwards in order to more evenly mix the flow

## Slide 6: New Test Setup

## Slide 7: 5/8- inch Holes in Air Distribution Tube
Air
Inlet

## Slide 8: Preliminary Measurements
While the unit is cold, air velocity was measured in the OSU with an anemometer
Left:
0.44 m/s
Center:
0.32-0.40 m/s
Right:
0 m/s
Air
Inlet

## Slide 9: Preliminary Measurements
While the unit is cold, pressure was measured in the OSU with digital manometer
120 Hole Plate
8 Hole Plate
Lower Plenum:
10.8 inch WC
0.389 Psi
Interspace Area:
0.4 inch WC
0.0144 Psi

## Slide 10: Preliminary Tests in the OSU
Four different honeycomb samples were tested in the OSU for comparative purposes
Each sample was tested five times
Sample | Thickness
Sample A | 1/8 in
Sample B | 11/16 in, white decorative
Sample C | 7/8 in
Sample D | 1/4 in, white decorative

## Slide 11: Preliminary Tests in the OSU Baseline Test Results: Average of 5 Tests Shown Per Sample; No Changes Have Been Done to the Original OSU Setup Yet

## Slide 12: Drawing of new setup

## Slide 13: Animation of New Setup

## Slide 14: Conclusion
New setup shows an even distribution of air flow in front of the sample face.
Will test materials in a hot OSU to understand how this setup affects the burning of samples

## Slide 15: Questions or Comments?
Tina Emami
  FAA William J. Hughes Technical Center
  ANG-E212 Materials Fire Test
  Building 275
  Atlantic City Int’l Airport, NJ 08405
  Tina.Emami@faa.gov
  609-485-4277