## Slide 1: Flow Visualization in the OSU
IAMFTFM
Tina Emami
October 29, 2018

## Slide 2: Airflow Project Goals
Create an adjustment to the current OSU apparatus in order to create an even and reproducible air flow.

## Slide 3: Test Setup
Aluminum oxide powder is seeded through the OSU
Laser light sheet is directed towards the side of the OSU and the PIV camera is placed perpendicular to this light sheet to capture seeding particles
Camera can capture data of size 96.64mm x 72.71mm
The width of the OSU fits 4 measurement frames
96.64mm
72.71mm
Measurement frame

## Slide 4
Measurement Location

## Slide 5: Measurement Location
The PIV camera is aligned to view the flow between the middle two glow bars

## Slide 6: New Measurement Redo
Airflow measurements at regular settings were redone ½ inch away from sample face to accurately measure velocities

## Slide 7: Background
Original Set Up
Bottom Air Inlet Set Up

## Slide 8: Background
Moved the location of the air inlet from the side of the OSU to the bottom to test imbalance in flow
  This created air circulation through the center of the OSU near the test sample, but created a more even upwards flow on both sides of the OSU

## Slide 9: Background cont.
Two Plate Setup

## Slide 10: Background cont.
Two Plate Setup

## Slide 11: Background cont.
One Plate Setup

## Slide 12: Background cont.
One Plate Setup

## Slide 13: New Test Setup
Air inlet was moved back to its original location
PVC tube with two rows of evenly spaced ¼” holes 45° from horizontal was constructed
Cap is glued to the end of the tube
Tube is placed in the bottom chamber of the OSU
Holes will be oriented to face downwards in order to more evenly mix the flow

## Slide 14: New Test Setup
OSU laying down on side
Bottom View

## Slide 15: New Test Setup

## Slide 16: New Test Setup

## Slide 17: New Test Setup Flow of Right End Location

## Slide 18: Potential new design

## Slide 19: Conclusion
New setup shows a slower but even distribution of air flow in front of the sample face.
Test second design
Testing in a hot OSU to understand how this setup affects the burning of samples

## Slide 20: Questions or Comments?
Tina Emami
  FAA William J. Hughes Technical Center
  ANG-E212 Materials Fire Test
  Building 275
  Atlantic City Int’l Airport, NJ 08405
  Tina.Emami@faa.gov
  609-485-4277