## Slide 1
Smoke Transport Modeling for
Cargo Bay Applications
Changmin Cao, May Corn, Vaidya Sankaran
United Technologies Research Center
Kenneth Bell
UTC Aerospace Systems
May 8, 2018
FAA Systems Working Group Meeting – Cologne, Germany – May 8, 2018

## Slide 2
Acknowledgements
FAA
  Matthew Karp
  Robert Ochs
UTC Aerospace Systems
FAA Systems Working Group Meeting – Cologne, Germany – May 8, 2018

## Slide 3: Cargo bay Detection system development
FAA Systems Working Group Meeting – Cologne, Germany – May 8, 2018
Substantial number of tests required to develop and certify detection system
Design and Optimize Detection System
Certify Detection System

## Slide 4: Model-based design vision: detection system development
FAA Systems Working Group Meeting – Cologne, Germany – May 8, 2018
Objective: Develop a model-based tool to augment and streamline certification process
Benefits:
Virtual tests
Parametric variations
Physical insight
Accelerate development
Cargo Bay Detection System Design Tool
Reduce number of flight certification tests
Reduce cost of certification

## Slide 5: Cargo bay Detection system design tool framework
FAA Systems Working Group Meeting – Cologne, Germany – May 8, 2018
Smoke generator
Flow rates, Size Distribution
Temperature, Velocity
Location
Smoke Transport in the Cargo Bay
Computational Fluid Dynamics (CFD) Model
Smoke Mass Dispersion (Function of space and time)
Ventilation
Location
Flow rates
Detector
Geometry
Placement
Input Parameters
Cargo Bay
Geometry
Obstructions
System Response Time of Detector Layout
Select promising designs to test
Detection System Performance?
Refine
models

## Slide 6: Model components
FAA Systems Working Group Meeting – Cologne, Germany – May 8, 2018
Smoke Source
Size distribution
Temperature
Velocity
Steady vs. transient
Smoke Transport to the ceiling
Large room features/obstructions
Small scale features – detector tray
Buoyancy Ventilation
Environmental conditions
System Response Time
Obscuration (smoke concentration) & transport time
Smoke Transport prediction depends on validity of Smoke Source simulation
First step: develop a CFD model to simulate the Smoke Generator
Smoke Transport CFD Model

## Slide 7: Smoke source: smoke generator
FAA Systems Working Group Meeting – Cologne, Germany – May 8, 2018
Smoke Generator
Particle size generation and velocity affected by
Heater size and arrangement
Atomization / Condensation
Flow rates
Difficult to characterize and generalize smoke generator
http://www.concept-smoke.co.uk/
Chart: Centerline Plume Temperature
| 0 | 0.30479999999999996 | 0.60959999999999992 | 0.91439999999999999 | 1.2191999999999998
Temp (deg C) | 66 | 43 | 30 | 28.5 | 25
Chart: Centerline Plume Velocity Range
| 0 | 0.30479999999999996 | 0.60959999999999992 | 0.91439999999999999 | 1.2191999999999998
Min. Velocity | 0.33528 | 0.58421 | 0.37084 | 0.29464 | 0.2794
Max. Velocity | 0.42673 | 0.76201 | 0.84837 | 0.76201 | 0.68073
Measurements from FAA – One Set of Operating Conditions
max
min

## Slide 8: Simulation tool & set-up
FAA Systems Working Group Meeting – Cologne, Germany – May 8, 2018
Fire Dynamics Simulator (FDS)
3-D, unsteady solver from NIST (version 6.6.0)
Large Eddy Simulation (LES)
Low Mach with Direct Poisson equation solver for pressure
Time Integration: 2nd order explicit predictor-corrector scheme
Smoke Generator Set-Up
Total cells: 1.62 million
Hexahedral cells
Non-uniform sized mesh
Parallel computing cluster (~100 cores)

## Slide 9: Smoke generator model
How should we model the injection of the smoke from the generator?
FAA Systems Working Group Meeting – Cologne, Germany – May 8, 2018
Evaluate the following Injection Approaches
Method 1: Inject aerosol as a distribution of particles
Realistic, but may be computationally expensive
Method 2: Inject aerosol as a gas
Reasonable if sub-micron particles follow the flow

## Slide 10: Smoke generator model
Initial Conditions at Smoke Generator Injection Plane
FAA Systems Working Group Meeting – Cologne, Germany – May 8, 2018
 | Particle Injection Method 1 | Aerosol-as-Gas Method 2
Aerosol flow rate | Oil + Carrier N2 | Mass fractions of Smoke and N2
Particle size distribution | derived from representative data | n/a
Temperature | Same initial temperature | 
Velocity | Same initial velocity | 
Turbulence intensity | Same initial turbulence intensity | 

## Slide 11: Qualitative comparison of flow fields
Aerosol-as-gas method produces similar plume features as particle injection method
FAA Systems Working Group Meeting – Cologne, Germany – May 8, 2018
Method 1: Particle injection
Method 2: Aerosol-as-gas
(kg/kg)
Temperature (0C)
Gas velocity (m/s)
Particle sizes
Temperature
Gas velocity
Mass fraction

## Slide 12: Quantitative comparison with data
FAA Systems Working Group Meeting – Cologne, Germany – May 8, 2018
Both injection methods (particle-based and gas-based) produce similar profiles
Centerline Plume Velocity
Centerline Plume Temperature
Chart: Offset height (m)
| 0 | 0.30479999999999996 | 0.60959999999999992 | 0.91439999999999999 | 1.2191999999999998
FAA Data Max. | 0.42673 | 0.76201 | 0.84837 | 0.76201 | 0.68073
FAA Data Min. | 0.33528 | 0.58421 | 0.37084 | 0.29464 | 0.2794
Particle_injection | 0.36911 | 0.4778 | 0.58856 | 0.67668 | 0.72034 | 0.75525 | 0.74862 | 0.78606 | 0.79786 | 0.78962 | 0.78429 | 0.79206 | 0.77218 | 0.80448 | 0.80494 | 0.73344 | 0.74137 | 0.72483 | 0.71901 | 0.70619 | 0.69701 | 0.7071 | 0.72336 | 0.71604 | 0.6926 | 0.68521 | 0.68111 | 0.67047 | 0.66988 | 0.68834 | 0.67299 | 0.66834 | 0.65578 | 0.66425 | 0.64737 | 0.64713 | 0.62894 | 0.60738 | 0.60835 | 0.62746
Aerosol-as-gas | 0.46079 | 0.62492 | 0.65814 | 0.68363 | 0.71495 | 0.73844 | 0.75089 | 0.75768 | 0.77262 | 0.76366 | 0.74163 | 0.73389 | 0.72633 | 0.70469 | 0.69 | 0.69784 | 0.67345 | 0.66087 | 0.6556 | 0.65062
Chart: Offset height (m)
| 0 | 0.30479999999999996 | 0.60959999999999992 | 0.91439999999999999 | 1.2191999999999998
FAA Data | 66 | 43 | 30 | 28.5 | 25
Particle-injection | 64.216 | 62.625 | 56.572 | 52.544 | 47.658 | 45.197 | 42.201 | 40.534 | 38.429 | 36.565 | 35.431 | 33.79 | 32.844 | 31.836 | 31.354 | 30.873 | 30.482 | 30.087 | 29.443 | 29.147 | 28.834 | 28.624 | 28.307 | 28.092 | 27.792 | 27.476 | 27.274 | 27.002 | 26.804 | 26.572 | 26.456 | 26.233 | 26.118 | 26.009 | 25.749 | 25.649 | 25.556 | 25.461 | 25.295 | 25.202
Aerosol-as-gas | 62.1066 | 53.2327 | 44.2842 | 39.3819 | 36.6542 | 35.3849 | 33.2211 | 32.0545 | 30.4878 | 29.7355 | 28.7915 | 28.0902 | 27.5422 | 26.9792 | 26.597 | 26.2015 | 25.8947 | 25.5834 | 25.3618 | 25.1882 | 24.9957
Simulations match the measured profile
Simulations fall within upper end of measurement range
FAA Data – Min Velocities
FAA Data – Max Velocities
FAA Data
Method 1: Particle Injection
Method 2: Aerosol as Gas

## Slide 13: Plume centerline particle size
Particle size distribution parameters do not vary significantly with height
FAA Systems Working Group Meeting – Cologne, Germany – May 8, 2018
Chart: Diameter (microns)
| Dv 10 | Dv 50 | Dv 90
POS1: injection plane | 0.14 | 0.24 | 0.41
POS2: 1.0 m | 0.145 | 0.25 | 0.41
POS3: 2.0 m | 0.15 | 0.275 | 0.43
20 cm x 20 cm x 20 cm cubes interrogated
Particle size distribution parameters
Results suggest that particles follow the flow
What happens when the plume is dispersed by cross-flowing ventilation?

## Slide 14: Plume centerline particle size: cross-flowing air present
Particle size distribution parameters do not change significantly as the plume is interacts with a crossflow
This scenario also suggests that particles follow the flow.
Plume can be modeled as a gas with constant particle size distribution
FAA Systems Working Group Meeting – Cologne, Germany – May 8, 2018
Chart: Diameter (microns)
| Dv 10 | Dv 50 | Dv 90
POS1: injection plane | 0.14 | 0.25 | 0.41
POS2: 1.0 m | 0.14 | 0.24 | 0.41
POS3: 1.5 m | 0.13 | 0.24 | 0.43
VENT
20 cm x 20 cm x 20 cm cubes interrogated
Particle size distribution parameters

## Slide 15: Quantitative comparison: centerline smoke concentrations
FAA Systems Working Group Meeting – Cologne, Germany – May 8, 2018
Gaseous injection method produces similar smoke distribution profiles as particle injection method
Chart: Height (m)
| 0.5 | 0.55127999999999999 | 0.60255999999999998 | 0.65385000000000004 | 0.70513000000000003 | 0.75641000000000003 | 0.80769000000000002 | 0.85897000000000001 | 0.91025999999999996 | 0.96153999999999995 | 1.0127999999999999 | 1.0641 | 1.1153999999999999 | 1.1667000000000001 | 1.2179 | 1.2692000000000001 | 1.3205 | 1.3717999999999999 | 1.4231 | 1.4743999999999999 | 1.5256000000000001 | 1.5769 | 1.6282000000000001 | 1.6795 | 1.7307999999999999 | 1.7821 | 1.8332999999999999 | 1.8846000000000001 | 1.9359 | 1.9872000000000001 | 2.0385 | 2.0897000000000001 | 2.141 | 2.1922999999999999 | 2.2435999999999998 | 2.2949000000000002 | 2.3462000000000001 | 2.3974000000000002 | 2.4487000000000001 | 2.5
Particle Injection | 0.89681 | 1 | 0.78182 | 0.48369 | 0.36373 | 0.28063 | 0.18367 | 0.079519 | 0.052889 | 0.012217 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 16: Summary—smoke generator simulation approach
FAA Systems Working Group Meeting – Cologne, Germany – May 8, 2018
 | Key Observations | Computational Time
Method 1: Particle Injection | Particles follow the flow Size distribution does not change | 3 hours - 9 hours
Method 2: Aerosol-as-Gas | Similar results as Method 1 Gas velocity Temperature Smoke concentration | 2 hours
Therefore, select Aerosol-as-Gas Method to simulate the smoke generator in a Cargo Bay Simulation
Computational time for Method 1 will increase in a closed room simulation because of particle accumulation
Method 2 sufficiently predicts velocity, temperature, smoke concentration profiles.

## Slide 17: Cargo bay simulation demonstration
Simulations conducted with the current smoke generator model to predict smoke transport in the cargo bay
- Varied smoke generator position, ventilation scenarios
FAA Systems Working Group Meeting – Cologne, Germany – May 8, 2018
Smoke transport into the detector tray
Additional data being acquired to validate transport models for the cargo bay
UTC Aerospace Systems
Cargo Bay Test Simulator

## Slide 18: Cargo bay smoke transport modeling: next steps
FAA Systems Working Group Meeting – Cologne, Germany – May 8, 2018
Characterization of Fires
Characterization of Smoke Generators
Assess Smoke Detection Performance via Simulation Methodology
Characterization of Transport Dynamics in Cargo Compartments
Mature tool to encompass smoke generated from fire sources