## Slide 1: Carbon Dioxide as Cargo Hold Fire Suppression Agent
IASFPWG Fall 2014
Paul Rohrbach and Rainer Beuermann

## Slide 2: Motivation
HFCs/Ketone no option due to overpressure phenomenon observed during MPS exploding aerosol can test
CFCs/ Halons
Inert Gases & CO2
Aerosols
Water
Inhibition
Cooling
Suffocation
Gaseous Agents
Fire Suppression Mechanism
Non-gaseous Agents
HFCs / Ketone

## Slide 3: Motivation
Inert Gases & CO2
Aerosols
Water
Inhibition
Cooling
Suffocation
Gaseous Agents
Fire Suppression Mechanism
Non-gaseous Agents
Corrosion & Certification
Operation (Freezing) & Certification
Many agents have thoroughly been considered in the past except CO2

## Slide 4: CO2 Systems in Aviation
CO2/N2 systems are operated onboard aircraft
Regulations/guidelines are in place for handling, manufacturing, shipment, operation, and maintenance of such systems
© AMSAFE BRIDPORT
Design / Engineering
Manufacturing / FAL
Operations / Maintenance

## Slide 5: Performance
Surface-Burning Fire

## Slide 6: Value and Risks
CO2
Clean / Nonconductive
SNAP
Good Heat Capacity
Good Penetration Capability
Preliminary MPS Tests
Liquefiable Gas
Zero Safety Margin
© K. Kallergis

## Slide 7: Technical Challenges
Lack of information on CO2/N2 gas mixtures (phase diagrams) covering the desired temperature range
Characteristics of these mixtures – mainly pressure vs temperature – need to be established
Risk of CO2 desublimation if system is not properly designed
Three-step approach formulated with research partner DLR to address technical challenges

## Slide 8: Technical Challenges - Approach
Page 8
Lab Tests
Pre-selection of CO2/inert gas mixture
Determination of filling density over required temp. range
Mid-Scale Tests
Validation of lab-scale test results
Preliminary MPS Tests
Preliminary tests scheduled for Q1- 2015
Comparison of results with theoretical models
Agent discharge tests (cylinderpipingnozzle)
Agent distribution tests in relevant environment

## Slide 9: CO2 Discharge Tests

## Slide 10: Concept
CO2 will be replaced over time with Nitrogen Enriched Air (NEA)
Cargo Fire Suppression
CO2/N2
Knock down Fire
  Guidance material available for gaseous agents / CS-25 AMC 25.851(c)
  For Knock-down part  system concept similar to State-of-the-Art System
  Standards/guidelines are available for handling, manufacturing, shipment, operation, and maintenance of CO2/N2 cylinders
NEA
Suppress Fire
What if we would use an escape slide cylinder and discharge it into the cargo hold ?

## Slide 11: Health and Safety
CO2/N2 systems seem to be technically feasible but health and safety issues need to be addressed and examined and technical benefits must be weighed against potential risks
FAR/CS Regulations already adressing health and safety issues associated with the use of fire suppressants:
  There must be means to exclude hazardous quantities of […] extinguishant […] from occupied areas to comply with the regulations
Risks for air cargo ground operation and maintenance personnel would need to be assessed

## Slide 12: Some Thoughts
What would generally be the difference between handling, shipping and maintaining an escape slide cylinder containing CO2/N2 and a fire suppression cylinder containing CO2/N2 ?
Could ground operation issues be managed per design and with procedures (discharge not to occur on ground while people in the cargo hold and cargo doors are open), with placards, training…?

## Slide 13: Finally
.....and now – please throw in your thoughts, perceptions, comments..…

## Slide 14
© Airbus Operations GmbH. All rights reserved. Confidential and proprietary document. This document and all information contained herein is the sole property of Airbus Operations GmbH. No intellectual property rights are granted by the delivery of this document or the disclosure of its content. This document shall not be reproduced or disclosed to a third party without the express written consent of Airbus Operations GmbH. This document and its content shall not be used for any purpose other than that for which it is supplied. The statements made herein do not constitute an offer. They are based on the mentioned assumptions and are expressed in good faith. Where the supporting grounds for these statements are not shown, Airbus Operations GmbH will be pleased to explain the basis thereof. AIRBUS, its logo, A300, A310, A318, A319, A320, A321, A330, A340, A350, A380, A400M are registered trademarks.